| Scenario | Force Calculations | Work Calculations |
| --- | --- | --- |
| A 50-N horizontal force pushes a 10-kg block across a rough surface (µk = 0.12) a distance of 15 meters. Draw the FBD Below: |  |  |
|  | Net Force | Net Work |
|  | Initial KE 0 Joules | Final KE | (KE |
| Questions: (a) When the net work on an object is positive, the object (select one) slows down speeds up doesn’t change speed (b) What is the final speed of the block? |
| A 10-kg block slides down an incline (µk = 0.10) a distance of 8.0 meters. Draw the FBD Below: |  |  |
|  | Net Force | Net Work |
|  | Initial KE | Final KE | (KE |
| Questions: (c) Which component of gravity does work in this problem? (Select one) Fg sin (15() Fg cos (15() (d) What is the final speed of the block? |
| A boy pulls his 22-kg wagon using a 55-N force, as shown, through a distance of 210 meters. The coefficient of kinetic friction between the cart and the ground is 0.25. Draw the FBD Below: |  |  |
|  | Net Force | Net Work |
|  | Initial KE | Final KE 400 J | (KE |
| Questions: (e) Which of the components of the 55 N force does work in this problem? (Select one) 55N sin(25() 55N cos(25() (f) What is the initial speed of the wagon? |
| Scenario | Force Calculations | Work Calculations |
| A crate (m = 10 kg) slides to a stop. Its initial velocity is v = 15 m/s to the right. The coefficient of friction between the block and the floor is 0.40. Draw the FBD Below: |  |  |
|  | Net Force | Net Work |
|  | Initial KE | Final KE | (KE |
| Questions: (g) What is the only force doing any work on this crate? (h) How far does the crate travel before coming to rest? |

Work Done By Gravity (Hmmm… Check This Out)

| Scenario | Calculate the Ramp Length | Calculate the Work Done By Gravity | Calculate the Block’s Speed at the Bottom of the Ramp * |
| --- | --- | --- | --- |
| A 10-kg block slides from rest down a frictionless ramp from a height of 5 meters. The angle of inclination is 20 degrees. |  |  |  |
| A 10-kg block slides from rest down a frictionless ramp from a height of 5 meters. The angle of inclination is 30 degrees. |  |  |  |
| A 10-kg block slides from rest down a frictionless ramp from a height of 5 meters. The angle of inclination is 40 degrees. |  |  |  |

Based on the data you just generated, what does the work done by gravity depend upon?

# Text boxes

Wnet = (KE = ½ m vf2 – ½ m vi2

Pre-AP Work-Kinetic Energy Practice

10 kg

20(

5.0 m

*Is gravity the only force doing work?

5.0 m

10 kg

30(

5.0 m

10 kg

40(

Pre-AP Work-Kinetic Energy Practice

50 Points