Balancing Torque Calculations:  The mobile below hangs from a ceiling so that the rods are perfectly horizontal.  Complete the calculations below to solve for the masses A and B:

- What is the weight of the 0.12 kg mass?

- What is the torque produced by the 0.12 kg mass about Axis 1?

- What is the weight of Mass A (Hint: the torque produced by mass A must balance with the torque produced by the 0.12 kg mass)?

- What is the value of Mass A?

- What is the weight of the lower bar?

- What is the total weight supported by string 1?

- What is the torque that the weight string 1 supports produces about Axis 2?

- What is the weight of Mass B (Hint: the torque produced by the weight of string 1 and all it supports must balance with the torque produced by Mass B)?

- What is the value of Mass B?

# Text boxes

0.12 kg

Mass A

Mass B

mbar = 0 .10 kg

0.08 m

0.70 m

0.24 m

0.50 m

mbar = 0 .20 kg

Axis 1

Axis 2

String 1