Basic Information:

Complete the following with “increases”, “decreases”, or “doesn’t affect”:

- All other things being equal, increasing the voltage in a circuit _____________ the current in a circuit.

- All other things being equal, decreasing the voltage in a circuit _____________ the current in a circuit.

- All other things being equal, increasing the resistance in a circuit ____________ the current in a circuit.

- All other things being equal, decreasing the resistance in a circuit ____________ the current in a circuit.

- Adding resistors in parallel in a circuit ________________ the equivalent resistance of a circuit.

- Adding resistors in series in a circuit ________________ the equivalent resistance of a circuit.

Complete the following:

- In general, longer wires have _________________ resistance than short wires.

- In general, wires with greater cross-sectional areas have ________________ resistance than wires with less cross-sectional area.

- In general, when current gets to a junction, it ______________ into branches.

- Circuit elements, such as resistors, have the same _______________ when connected in series.

- Circuit elements, such as resistors, have the same _______________ when connected in parallel.

- The change in electric potential (voltage) as you traverse a single closed loop in a circuit is ____________.

- The voltage across a resistor in a circuit is equal to __________________.

- For EACH of the two circuits shown, rank the current at the labeled points in the circuit, greatest first.  Assume that batteries and bulbs are identical:

Equations: Identify the variables in the following equations:

Show ALL your work (or provide adequate explanation) to find the unknowns for each circuit and complete the tables.

# Text boxes

Name ________________________

Pre-AP Physics       Period _____

3.0 (

4.0 (

20 V

6.0 (

I = 2.0 A

|  | Current (C/s) | Voltage Across (J/C) | Power Output (J/s) |
| --- | --- | --- | --- |
| 4-( |  |  |  |
| 3-( |  |  |  |
| 6-( |  |  |  |
| R1 |  |  |  |
| Battery |  |  |  |

R1

|  | Current (C/s) | Voltage Across (J/C) | Power Output (J/s) |
| --- | --- | --- | --- |
| R1 |  |  |  |
| 6.0-( |  |  |  |
| 2.0-( |  |  |  |
| Battery |  |  |  |

2 V

R1

6.0 (

2.0 (

8.0 V

|  | Current (C/s) | Voltage Across (J/C) | Power Output (J/s) |
| --- | --- | --- | --- |
| 12.0-( |  |  |  |
| 3.0-( |  |  |  |
| 10.0-( |  |  |  |
| 2.0-( |  |  |  |
| 8.0-( |  |  |  |
| Battery |  |  |  |

| Equivalent Resistance For Circuit: | Current Through Battery: |
| --- | --- |
| Voltage Across 5-(: | Voltage Across 4-( |
| Voltage Across 2-(: | Current in 4-( |
| Voltage Across 12-(: | Current in 12-( |