Big Ideas:  Current (symbolized by “I”) is the flow rate of charge in the different branches of a circuit.

By definition, it is the amount of charge that passes through part of a circuit per unit time:

The typical units for current are coulombs/second (C/s).  1 C/s is 1 Ampere (Amperes are often called “amps”).

We draw the direction of current in a circuit to point in the direction a positive charge would move (if they moved).

A junction is a point where more than two wires meet in a circuit (junctions have been labeled using letters in the circuits below).

Junction Rule: The amount of current that flows into a junction is equal to the amount of current that flows out of a junction.

Instructions:  For each of the following circuits, (a) Draw and label the current through each branch.  (b) Write the equations for each junction, then (c) solve for the current in each circuit element to complete the table.

| Circuit Element | R1 | R2 | R3 | R4 | R5 | Battery |
| --- | --- | --- | --- | --- | --- | --- |
| Current In | 8 A | 2 A |  |  |  |  |

| Circuit Element | R1 | R2 | R3 | R4 | R5 | R6 | Battery |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Current In | 2 A | 4 A |  |  |  |  | 10 A |

| Circuit Element | R1 | R2 | R3 | R4 | R5 | R6 | Battery |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Current In | 2 A | 1 A |  | 2 A |  |  | 5 A |

| Circuit Element | R1 | R2 | R3 | R4 | R5 | R6 | Battery |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Current In | 3 A | 9 A | 2A | 3 A |  |  |  |

| Circuit Element | R1 | R2 | R3 | R4 | R5 | R6 | R7 | Battery |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Current In | 8 A | 2 A |  | 3 A |  |  |  |  |

# Text boxes

25 Points

Equations for Junctions A – B:

R1

R3

R2

R5

(

R4

24 V

A

6 (

4 (

12 (

5 (

2 (

2 (

12 V

B

R1

R3

R4

R2

14 V

A

B

C

D

Equations for Junctions A – D:

Equations for Junctions A – D:

R2

R1

R3

(

R6

R5

R4

12 V

A

B

D

C

Equations for Junctions A – F:

R2

R4

R1

R3

R5

R6

12.0 V

A

B

C

D

E

F

R6

R2

R4

R3

R7

R1

10 V

R5

A

B

C

D

Equations for Junctions A – D: