- If you shook the end of a rope up and down three times each second, what would be the period of the waves generated on the rope?  What would be the frequency? (0.33 sec, 3 Hz)

- A wave of amplitude 0.75 m interferes with a second wave of amplitude 0.53 m.  Find the minimum possible amplitude if the interference is destructive.  Find the maximum possible amplitude if the interference is constructive.  (Ad = 0.22 m, Ac = 1.28 m)

- A wave with a frequency of 60 Hz has a speed of 12 m/s in a particular medium.  (a) What is the wavelength? (b) If the wave is transmitted into another medium in which it is propagated at a speed of 20 m/s, what is the new wavelength? (The frequency remains the same.) (0.2 m, 1/3 m)

- A student reading her physics book on a lake dock notices that the distance between two incoming wave crests is about 2.4 m, and then measures the time of arrival between adjacent wave crests to be 1.6 seconds.  What is the wavelength (() of the waves?  What is the frequency of the wave?  What is the approximate speed of the waves? (( = 2.4 m, f = 0.625 Hz, v =1.5 m/s)

- The range of sound audible to the human ear has frequencies from about 20 Hz to 20,000 Hz.  If the speed of sound in air is 345 m/s, what are the limits of this audible range in wavelengths? (range of ( = 17.25 m to 0.01725 m)

- A sonar generator on ship produces periodic ultrasonic waves at a frequency of 2.5 MHz (1 MHz = 1 x106 Hz).  The wavelength of the waves in seawater is 4.8 x 10-4 m. What is the speed of sound waves in water?  When the generator is directed downward, an echo reflected from the ocean floor is received 16.7 s later.  How deep is the ocean at that point? (v = 1200 m/s, d = 10020 m)

7.	A nylon guitar string has a linear density ( = .0072 kg/m and is tuned so that the tension (() in the string is 150 N.  The equation below relates the speed of a wave on a string to linear density and tension:

8.	The length of the string between its fixed supports is 0.90 meters. Calculate the (a) speed, (b) wavelength, and (c) frequency of the wave that produces the third harmonic standing wave.  (144 m/s, ( = 1.8 m, f = 241 Hz)

9.	The string from problem 1 is tuned so that it now has a tension of 200 N (assume that the linear density doesn’t change).  The string is plucked so that the first harmonic is produced.  What frequency is heard? (92.6 Hz)

10.	What are the three lowest frequencies for standing waves on a wire 10.0 meters long if the traveling wave speed is 160 m/s? (8 Hz, 16 Hz, and 24 Hz)

11. 	The graph to the right shows three waveforms.  Which waveform represents the sum of the other two?

# Text boxes

Pre-AP Waves Homework

A

# B

C